## Slide 1: Hornet 7.0 Software Workshop #2

## Slide 2
Sensors

## Slide 3
What are sensors?
“a device that responds to a physical stimulus and transmits a resulting impulse”
Stimulus
Sensor
Signal

## Slide 4
Why do we need sensors?
To locate ourselves and navigate
To understand our environment
To detect failure
To control our vehicle

## Slide 5
Location
Location is normally described as a pose which consists of:
(x,y,z) co-ordinates (a.k.a heave,surge, sway)
Roll, pitch and yaw (describes orientation)

## Slide 6
Position

## Slide 7
Locating ourselves underwater

## Slide 8
IMU
Inertial Measurement Unit
Combination of :
Accelerometer
Gyroscope
Magnetometer

## Slide 9
Accelerometer
Measures acceleration in the x,y,z axis
s = ∫ v dt = ∬ a dtdt〗^2 dt〗^2 a= s = dv/dt=(dS^2)/〖dt〗^2
Can be used to measure gravity
Double integral causes drift

## Slide 10
Gyroscope
Measures angular velocity
Can be used to correct for rotation as compass can respond slowly
Responds quickly
Has drift

## Slide 11
Magnetometer
Responds slowly to change in magnetic field
Detects strength of the magnetic field in the x,y,z axis
Can be used to determine true north
Requires calibration

## Slide 12
Depth Sensor
Uses pressure to determine depth
Fairly accurate

## Slide 13
Doppler Velocity Log
Emits a sound ping and waits for its echo
Echo is often of a shifted frequency due to doppler effect
Measures velocity
Expensive

## Slide 14
Optical Flow
Cheap. Easy to implement
Can measure velocity

## Slide 15
Errors
Sensors have their own set of measurement errors.
Even if these errors are small , they accumulate overtime
3) Sensor fusion is performed to correct uncertainties
4) Algorithms are also used:
a) kalman filter
b) madgwick filter
c) particle filter

## Slide 16
Sensors that understand environment
Camera
Radar/Lidar
Chemical sensors (never used by us before)
Others. Designed specifically for the task that is required to be carried out.

## Slide 17
Other uses
Detect internal problems
Pressure
Humidity
Temperature

## Slide 18
Controls

## Slide 19
What are controls
•Controls is a vast and complex field in robotics
•Generally we have a controller, a feedback and a setpoint.

## Slide 20
Examples
PID control
Bang-bang
Fuzzy Logic
And many more….

## Slide 21
Live Demo

## Slide 22
A general guide to tuning PID
Step 1 | Set all the gains to Zero
Step 2 | Increase the P gain until the response to a disturbance is steady oscillation
Step 3 | Increase the D gain until the oscillations goes away (i.e. it's critically damped).

## Slide 23
A general guide to tuning PID
Step 4 | Repeat steps 2 and 3 until increasing the D gain does not stop the oscillations.
Step 5 | Set P and D to the last stable values.
Step 6 | Increase the I gain until it brings you to the setpoint with the number of oscillations desired (normally zero but a quicker response can be achieved if you don't mind a couple oscillations of overshoot)

## Slide 24
Now it’s your turn!

## Slide 25
Assignment 2:
•See the PID control demo in ./assignment2-demo
Todo:
Do not edit simulator.py (you can take a look though)
Add in missing subscribers
PID equation
PID values

## Slide 26
Challenge Yourself: Don’t Google/Stackoverflow the answer.
As we move on to more challenging topics, you are less likely to find a solution online.
Often we only get hints to finding the solution in the form of pseudocode or math equations.
So put your problem-solving skills to the test and try to convert this PID equation into working code.

## Slide 28
ΔT
∫≈Σ

## Slide 29
ΔT
T T+ΔT
Where is ΔT?